## Slide 1: Standardizing the Kinnear Limit of Stokesian Settling (LOSS) parameter using image data analysis
Ola Olagunju, Tim Van Winckel, William Mancell-Egala, Nirmaan Shanker, David Kinnear, Ahmed Al-Omari, Sudhir Murthy, Kimberly Jones and Haydée De Clippeleir

## Slide 2: Background
Sludge Recovery
Influent
Effluent
Solids Flux
Clarifiers are a limiting step in wastewater treatment processes
Poor settling contributes to clarifier failures
  SLR and SOR failures
  Reduced effluent quality
  Reduced activated sludge recovery
SLR – Solids loading rate, kg/day·m²
SOR – Surface overflow rate, m³/hr·m²

## Slide 3: Background
Which settling profile is preferred in clarifiers?
B)
A)
Hindered Settling (slow)
CSV < 0.6 m/h
Flocculent Settling (fast)
CSV: 0.6 – 1.5 m/h

## Slide 4: Some Clarifier/Settling Techniques
Sludge Bed Detectors
Sludge Volume Index (SVI) and DSVI
State Point Analysis (SPA)
Markland Specialty Engineering Ltd.
Biological Waste Treatment Expert
CB Skoura et al., 2016

## Slide 5: Limit of Stokesian Settling (LOSS)
Hindered/Compression
Flocculent
Non-settleable solids
Discrete
Concentration (g/L)
Settling velocity (m/h)
Settling velocity model, Mancell-Egala et al., 2016
LOSS
Aims of parameter
  Capture transition from flocculent to hindered
  Provide maximum concentration to enter the clarifier feed well

## Slide 6: Identifying the LOSS Concentration
Original method involves taking video of settling sludge
Graphing color intensities from flocculent to hindered sludge
LOSS concentration was when slope of color intensity was greater than 5 (1cm ~ 250 pixels)
Flocculent MLSS
Slope < 5
Hindered MLSS
Slope > 5

## Slide 7: Identifying the LOSS Concentration
Issues with this method in identifying LOSS
  Ease of reproducibility
  Slope definition ambiguous and subjective
  Time of settling (secs) not standardized
  Light conditions not standardized
All at MLSS of 1000 mg/L
50s, 5 bri.
Brightness from 0 – 255 (black to white)
50s, 75 bri.
10s, 25 bri.
10s, 200 bri.
80s, 25 bri.
20s, 25 bri.

## Slide 8: Goals of Research
Develop new methods for identifying LOSS
  Straightforward for anyone
  Simply reproducible
  Standardize for different settling times and brightness
Rod Engineering

## Slide 9: Approach
Secondary WEST
Secondary Clarifiers
BNR Nitrification
BNR Clarifiers
Blue Plains WWTP, DC 370-518 MGD raw sewage
Secondary EAST

## Slide 10: Approach
Secondary EAST
Secondary WEST
BNR
Samples

## Slide 11: Approach
Video Image analysis on settling sludge
Hindered to flocculent MLSS
Well mixed mixture
  100 rpm for 10 mins
  Pictures taken every 10 secs after mixing is stopped
Changing light conditions
  Adjusting camera brightness
Video analysis
HD camera
Tripod
Jar
LED light pad

## Slide 12: Approach
Converted pictures to 16-bit grayscale (black to white, 0-255)
Sorted pictures
  High to low concentration
  At the same settling time
  At the same Light Intensity/brightness
Significant change in grayscale intensity profile between pictures as concentration decreased indicated LOSS

## Slide 13: Approach
Three methods to find significant change
Linear Fit
  Slope and R²
B,
Y-Intercept
Y, Grayscale Intensity
X, Jar Height
Simple Linear Regression
Top 1/3rd of Jar

## Slide 14: Approach
Three methods to find significant change
Linear Fit
  Slope and R²
Sigmoid Fit
  B, C and Fit error
C, Inflection point
K, Upper Asymptote
A, Lower Asymptote
Y, Grayscale Intensity
X, Jar Height
Generalized Logistic Function

## Slide 15: Approach
Three methods to find significant change
Linear Fit
  Slope and R²
Sigmoid Fit
  B, C and Fit error
Noise Analysis
  Mean std. deviation
Standard deviation
Flocculent
Hindered

## Slide 16: Approach
Three methods to find significant change
Linear Fit
  Slope and R²
Sigmoid Fit
  B, C and Fit error
Noise Analysis
  Mean std. deviation
Standard deviation
Y, Grayscale Intensity
X, Pixel index
n = 100
n = 100
n = 100
…

## Slide 17: Approach
Three methods to find significant change
Linear Fit
  Slope and R²
Sigmoid Fit
  B, C and Fit error
Noise Analysis
  Mean std. deviation
Standard deviation
Standard deviation
X, Pixel index/100

## Slide 18
Intensity
Pixel index
Intensity
Pixel index
Intensity
Pixel index
σ
Pixel index
Pixel index
Pixel index
σ
σ
Sigmoid Fit
Fitted Sigmoid Curve
Noise Analysis
Mean σ
Hindered
Flocculent
Around LOSS
B = 0.0363, C = 548.1, Fit error = 1.919
B = 0.0047, C = 1100, Fit error = 3.281
B = 0.0015, C = 1547, Fit error = 9.752
Mean σ = 0.1576
Mean σ = 0.1036
Mean σ = 0.0733
Linear Fit
Intensity
Pixel index
Intensity
Pixel index
Intensity
Pixel index
Regression Line
Slope = -0.1322, R² = 0.9081
Slope = -0.1413, R² = 0.6159
Slope = -0.0752, R² = 0.9986

## Slide 19
Percent change or Threshold > 50%
LOSS Concentration
slope for every three points
MLSS concentration (mg/L)
Parameters (Flocculent)
Slope of parameters
Parameters (Hindered)
Parameters e.g. Slope, R², B, C, Fit error, Mean σ, from each concentration
Slope of parameters

## Slide 20: Findings
Compared three methods
  Linear fit, Sigmoid fit, Noise Analysis
Compared six (6) light conditions
  5, 10, 25, 50, 75, 200 intensities
Compared ten (10) settling times
  0, 10, 20, 30, 40, 50, 60, 70, 80, 90 secs

## Slide 21: Criteria for evaluation
1. Is a LOSS value consistently measurable?
      For same method
      For same light condition
      For same settling time
2. Is the standard error between LOSS values less than ± 100 mgTSS/L?
      For same method
      Under practical light conditions and settling times that passed criteria 1

## Slide 22: Consistency of determination
Sigmoid Fit
Noise Analysis
Linear Fit
Failed LOSS determination
Successful LOSS determination
Practical range for use
Success rate across all samples
Linear – 87%
Sigmoid – 55%
Noise – 97%

## Slide 23
Sigmoid fitting was unworkable in some pictures due to their intensity profile
Intensity
Pixel index
Intensity
Pixel index
B = 0.0363, C = 548.1, Fit error = 1.919
Intensity
Pixel index
B = 0.0015, C = 1547, Fit error = 9.752
Intensity
Pixel index
Fitted Sigmoid Curve

## Slide 24: Consistency of determination
Too high/low brightness reduces information capacity
  More apparent in flocculent profiles
Intensity
Pixel index
5 LI
50 LI
200 LI
Flocculent  1000 MLSS, 30 secs of settling

## Slide 25: Consistency of determination
Too high/low brightness reduces information capacity
  More apparent in flocculent profiles
Intensity
Pixel index
5 LI
50 LI
200 LI
Hindered  4000 MLSS, 30 secs of settling

## Slide 26: Consistency of determination
Too high/low brightness reduces information capacity
  More apparent in flocculent profiles
Intensity
Pixel index
Intensity
Pixel index
50 LI, 30 secs settling
200 LI, 30 secs settling
Intensity
Pixel index
5 LI, 30 secs settling

## Slide 27: Consistency of determination
High settling time also reduces information capacity
  More apparent at high light intensities
  Flocculent profiles ‘look’ hindered or in compression
Intensity
Pixel index
Intensity
Pixel index
50 LI, 80 secs settling
200 LI, 80 secs settling
Intensity
Pixel index
5 LI, 80 secs settling

## Slide 28
Intensity
Pixel index
5 LI, 80 secs settling
Intensity
Pixel index
50 LI, 80 secs settling
5 LI, 80 secs, 1000 MLSS
50 LI, 80 secs, 1000 MLSS
Intensity
Pixel index
200 LI, 80 secs settling
200 LI, 80 secs, 1000 MLSS

## Slide 29: Precision of LOSS values
Sigmoid Fit
Noise Analysis
Linear Fit
Failed LOSS determination
Successful LOSS determination
Practical range for use

## Slide 30: Precision of LOSS values
Std. error (± mgTSS/L)
Secondary EAST
Secondary WEST
BNR
Std. error (± mgTSS/L)
Sample
Sigmoid Fit
Linear Fit
Criteria 2 ( < 100 mgTSS/L)
Std. error (± mgTSS/L)
Sample
Noise Analysis

## Slide 31
Sigmoid Fit
Noise Analysis
Linear Fit
Secondary EAST
Secondary WEST
BNR
Sample
Sample

## Slide 32: Final Thoughts
Noise Analysis was the most reliable method for calculating the LOSS concentration
Suitable light conditions and settling times for LOSS experiments were determined
The Limit of Stokesian Settling (LOSS) could be used as a parameter for clarifier operation

## Slide 33: References
Mancell-Egala, William ASK, David J. Kinnear, Kimberly L. Jones, Haydee De Clippeleir, Imre Takacs, and Sudhir N. Murthy. "Limit of stokesian settling concentration characterizes sludge settling velocity." Water research 90 (2016): 100-110.
Takács, Imre, Gilles G. Patry, and Daniel Nolasco. "A dynamic model of the clarification-thickening process." Water research 25, no. 10 (1991): 1263-1271.

## Slide 34
Thanks for your attention!
Contact Information
Ola Olagunju
ola.olagunju@dcwater.com

## Slide 35: Additional Slides

## Slide 36: Limit of Stokesian Settling (LOSS)
Pros
  Capture transition from flocculent to hindered
  Provide maximum concentration to enter the clarifier feed well
Cons
  NSS fraction